## Slide 1
CS 61C, Fall 2024 @ UC Berkeley
Slides credit: Dan Garcia, Bora Nikolic, Peyrin Kao
Slides template credit: Josh Hug, Lisa Yan
Pipelining
Lectures 21–22
Announcements:
Dan's office hours on Fri, Oct 18 cancelled.
Don't discuss midterm until grades are released.
No midterm grade ETA right now, but reminder that we have a clobber policy.

## Slide 2: Measuring Performance
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 3: The Single-Cycle RISC-V Datapath
Behold: Our circuit for running RISC-V instructions. We built this in the last 4 lectures.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
inst[11:7]
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst[31:0]
PC
2
0
1
0
1
1
0
0
1
IMEM
PC
inst
ALU
PC+4

## Slide 4: Instruction Timing
What is the clock period of our datapath circuit?
Determined by longest path (lw).
Clock period: 800ps.
Frequency: 1/800ps = 1.25 GHz.
1.25 billion instructions per second.
Can we improve our datapath performance?
What does it mean to improve performance?
Quicker response time = one job finishes faster?
More jobs per unit time?
Longer battery life?
instr | Time taken per stage (in ps): |  |  |  |  | Total time taken:
 | IF | ID | EX | MEM | WB | 
add | 200 | 100 | 200 |  | 100 | 600ps
beq | 200 | 100 | 200 |  |  | 500ps
jal | 200 | 100 | 200 |  | 100 | 600ps
lw | 200 | 100 | 200 | 200 | 100 | 800ps
sw | 200 | 100 | 200 | 200 |  | 700ps
This table shows some example timings.
Some cells are empty if the instruction doesn't use that stage.

## Slide 5: Analogy: Transportation
Consider two different vehicles:
For a 50 mile trip (assuming instant return trips)...
 | Sports Car | Bus
Passenger Capacity: | 2 | 50
Travel Speed: | 200 mph | 50 mph
Gas Mileage: | 5 mpg | 2 mpg
 | Sports Car | Bus
Travel Time: | 15 min | 60 min
Time for 100 passengers: | 750 min (50 trips) | 120 min (2 trips)
Gallons per passenger: | 5 gallons | 0.5 gallons

## Slide 6: Measuring Performance in Computers
We'll look at 3 different measures of computer performance:
Transportation Analogy | In a Computer
Trip Time | Program execution time (Example: Time to update display)
Time for 100 passengers | Throughput (Example: Number of server requests handled per hour)
Gallons per passenger | Energy per task (Example: How many movies you can watch per battery charge)

## Slide 7: Optimizing Time Per Program
The "Iron Law" of processor performance:
There are 3 components for optimizing the time it takes to execute a program.
Time | = | Instructions | Cycles | Time
Program |  | Program | Instruction | Cycle

## Slide 8: Optimizing Time Per Program (1/3)
The "Iron Law" of processor performance:
Instructions per program determined by:
The task we're trying to do.
The algorithm we implement, e.g. θ(N2) or θ(N).
The programming language we use.
The compiler we use.
The instruction set architecture (ISA) we use, e.g. x86 or RISC-V.
Time | = | Instructions | Cycles | Time
Program |  | Program | Instruction | Cycle

## Slide 9: Optimizing Time Per Program (2/3)
The "Iron Law" of processor performance:
Average clock cycles per instruction (CPI) determined by:
The instruction set architecture (ISA).
Processor implementation and microarchitecture, e.g. our datapath design.
Examples:
For the datapath we made, CPI = 1.
For complex instructions (e.g. strcpy), CPI > 1.
We'll see CPI < 1 processors later.
Time | = | Instructions | Cycles | Time
Program |  | Program | Instruction | Cycle

## Slide 10: Optimizing Time Per Program (3/3)
The "Iron Law" of processor performance:
Time per cycle (1/frequency) determined by:
Processor microarchitecture: Critical path through logic gates.
Technology: How many transistors fit in a given space.
Power budget: Lower voltages reduce transistor speed.
Time | = | Instructions | Cycles | Time
Program |  | Program | Instruction | Cycle

## Slide 11: Optimizing Time Per Program
The "Iron Law" of processor performance:
Time | = | Instructions | Cycles | Time
Program |  | Program | Instruction | Cycle
 | Processor A | Processor B
# Instructions | 1 million | 1.5 million
Average CPI | 2.5 | 1
Clock rate f | 2.5 GHz | 2 GHz
Execution time | 1 ms | 0.75 ms
Processor B is faster for this task, despite executing more instructions and having a slower clock rate!

## Slide 12: Optimizing Energy Per Program (1/2)
There are 2 components for optimizing the energy it takes to execute a program.
We already saw instructions per program earlier – it appears in this equation, too.
Energy | = | Instructions | Energy
Program |  | Program | Instruction

## Slide 13: Optimizing Energy Per Program (2/2)
There are 2 components for optimizing the energy it takes to execute a program.
Energy per instruction = CV2
C = capacitance. Depends on hardware technology and processor features.
V = supply voltage.
To improve performance, we can reduce capacitance and voltage.
Newer processors improve efficiency from Moore’s law and lower supply voltage.
Reducing supply voltage too far causes “leakage power” - transistor switches don’t fully turn off.
In recent years, it's gotten harder to reduce supply voltage.
Energy | = | Instructions | Energy
Program |  | Program | Instruction

## Slide 14: Optimizing Tasks Per Second
The energy "Iron Law":
Energy efficiency is a key metric in all computing devices.
If system is constrained by power, we need better energy efficiency to get more performance at the same power.
For energy-constrained systems, we need better energy efficiency to prolong battery life.
Tasks | = | Joules | Tasks
Second |  | Second | Joule
Performance |  | Power | Energy Efficiency

## Slide 15: Pipelining Analogy: Laundry
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 16: Pipelining Analogy: Laundry
Andrew, Bora, Caroline, Dan are doing laundry.
Each person needs to Wash, Dry, Fold, and Stash.
Wash using the washer takes 30 mins.
Dry using the dryer takes 30 mins.
Fold using the table takes 30 mins.
Stash using the drawers takes 30 mins.

## Slide 17: Laundry Timing Diagram
Example: From 2:00 to 2:30, Andrew is folding.
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30
Andrew | Wash | Dry | Fold | Stash |  | 
Bora |  |  |  |  |  | 
Caroline |  |  |  |  |  | 
Dan |  |  |  |  |  | 
Order of people.
Time of day.

## Slide 18: Sequential Laundry
Naive approach: Andrew does everything, then Bora does everything, and so on.
How long for everybody to finish laundry? 8 hours.
How long for one person to do their laundry? 2 hours.
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00 | 4:30 | 5:00 | 5:30 | 6:00 | 6:30 | 7:00 | 7:30 | 8:00 | 8:30
Andrew | Wash | Dry | Fold | Stash |  |  |  |  |  |  |  |  |  |  |  | 
Bora |  |  |  |  | Wash | Dry | Fold | Stash |  |  |  |  |  |  |  | 
Caroline |  |  |  |  |  |  |  |  | Wash | Dry | Fold | Stash |  |  |  | 
Dan |  |  |  |  |  |  |  |  |  |  |  |  | Wash | Dry | Fold | Stash

## Slide 19: Sequential Laundry
Can we do better than this?
Idea: When Andrew's drying, nobody is using the washer.
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00 | 4:30 | 5:00 | 5:30 | 6:00 | 6:30 | 7:00 | 7:30 | 8:00 | 8:30
Andrew | Wash | Dry | Fold | Stash |  |  |  |  |  |  |  |  |  |  |  | 
Bora |  |  |  |  | Wash | Dry | Fold | Stash |  |  |  |  |  |  |  | 
Caroline |  |  |  |  |  |  |  |  | Wash | Dry | Fold | Stash |  |  |  | 
Dan |  |  |  |  |  |  |  |  |  |  |  |  | Wash | Dry | Fold | Stash

## Slide 20: Pipelined Laundry
Pipelined approach: While Andrew uses the Dryer, Bora can use the Washer.
How long for everybody to finish laundry? 3.5 hours.
How long for one person to do their laundry? 2 hours. (Same as before!)
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00
Andrew | Wash | Dry | Fold | Stash |  |  | 
Bora |  | Wash | Dry | Fold | Stash |  | 
Caroline |  |  | Wash | Dry | Fold | Stash | 
Dan |  |  |  | Wash | Dry | Fold | Stash

## Slide 21: Pipelined Laundry
At any given moment in time, multiple people are in the system.
Different people are using different resources at the same time.
Example: At 2:30, Dan is using the Washer, Caroline is using the Dryer, and so on.
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00
Andrew | Wash | Dry | Fold | Stash |  |  | 
Bora |  | Wash | Dry | Fold | Stash |  | 
Caroline |  |  | Wash | Dry | Fold | Stash | 
Dan |  |  |  | Wash | Dry | Fold | Stash

## Slide 22: Pipelined Laundry
Over time, one person uses each of the resources, in order.
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00
Andrew | Wash | Dry | Fold | Stash |  |  | 
Bora |  | Wash | Dry | Fold | Stash |  | 
Caroline |  |  | Wash | Dry | Fold | Stash | 
Dan |  |  |  | Wash | Dry | Fold | Stash

## Slide 23: Filling and Draining the Pipeline
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00 | 4:30 | 5:00 | 5:30 | 6:00 | 6:30
Andrew | W | D | F | S |  |  |  |  |  |  |  | 
Bora |  | W | D | F | S |  |  |  |  |  |  | 
Caroline |  |  | W | D | F | S |  |  |  |  |  | 
Dan |  |  |  | W | D | F | S |  |  |  |  | 
Eddy |  |  |  |  | W | D | F | S |  |  |  | 
Jero |  |  |  |  |  | W | D | F | S |  |  | 
Myrah |  |  |  |  |  |  | W | D | F | S |  | 
Rosalie |  |  |  |  |  |  |  | W | D | F | S | 
Peyrin |  |  |  |  |  |  |  |  | W | D | F | S
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00 | 4:30 | 5:00 | 5:30 | 6:00 | 6:30
Andrew | W | D | F | S |  |  |  |  |  |  |  | 
Bora |  | W | D | F | S |  |  |  |  |  |  | 
Caroline |  |  | W | D | F | S |  |  |  |  |  | 
Dan |  |  |  | W | D | F | S |  |  |  |  | 
Eddy |  |  |  |  | W | D | F | S |  |  |  | 
Jero |  |  |  |  |  | W | D | F | S |  |  | 
Myrah |  |  |  |  |  |  | W | D | F | S |  | 
Rosalie |  |  |  |  |  |  |  | W | D | F | S | 
Peyrin |  |  |  |  |  |  |  |  | W | D | F | S
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00 | 4:30 | 5:00 | 5:30 | 6:00 | 6:30
Andrew | W | D | F | S |  |  |  |  |  |  |  | 
Bora |  | W | D | F | S |  |  |  |  |  |  | 
Caroline |  |  | W | D | F | S |  |  |  |  |  | 
Dan |  |  |  | W | D | F | S |  |  |  |  | 
Eddy |  |  |  |  | W | D | F | S |  |  |  | 
Jero |  |  |  |  |  | W | D | F | S |  |  | 
Myrah |  |  |  |  |  |  | W | D | F | S |  | 
Rosalie |  |  |  |  |  |  |  | W | D | F | S | 
Peyrin |  |  |  |  |  |  |  |  | W | D | F | S
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00 | 4:30 | 5:00 | 5:30 | 6:00 | 6:30
Andrew | W | D | F | S |  |  |  |  |  |  |  | 
Bora |  | W | D | F | S |  |  |  |  |  |  | 
Caroline |  |  | W | D | F | S |  |  |  |  |  | 
Dan |  |  |  | W | D | F | S |  |  |  |  | 
Eddy |  |  |  |  | W | D | F | S |  |  |  | 
Jero |  |  |  |  |  | W | D | F | S |  |  | 
Myrah |  |  |  |  |  |  | W | D | F | S |  | 
Rosalie |  |  |  |  |  |  |  | W | D | F | S | 
Peyrin |  |  |  |  |  |  |  |  | W | D | F | S
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00 | 4:30 | 5:00 | 5:30 | 6:00 | 6:30
Andrew | W | D | F | S |  |  |  |  |  |  |  | 
Bora |  | W | D | F | S |  |  |  |  |  |  | 
Caroline |  |  | W | D | F | S |  |  |  |  |  | 
Dan |  |  |  | W | D | F | S |  |  |  |  | 
Eddy |  |  |  |  | W | D | F | S |  |  |  | 
Jero |  |  |  |  |  | W | D | F | S |  |  | 
Myrah |  |  |  |  |  |  | W | D | F | S |  | 
Rosalie |  |  |  |  |  |  |  | W | D | F | S | 
Peyrin |  |  |  |  |  |  |  |  | W | D | F | S
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00 | 4:30 | 5:00 | 5:30 | 6:00 | 6:30
Andrew | W | D | F | S |  |  |  |  |  |  |  | 
Bora |  | W | D | F | S |  |  |  |  |  |  | 
Caroline |  |  | W | D | F | S |  |  |  |  |  | 
Dan |  |  |  | W | D | F | S |  |  |  |  | 
Eddy |  |  |  |  | W | D | F | S |  |  |  | 
Jero |  |  |  |  |  | W | D | F | S |  |  | 
Myrah |  |  |  |  |  |  | W | D | F | S |  | 
Rosalie |  |  |  |  |  |  |  | W | D | F | S | 
Peyrin |  |  |  |  |  |  |  |  | W | D | F | S
The ideal speedup for everyone to finish is 4x, since 4 things are happening at once.
Limited by:
Startup costs. "Filling" the pipeline.
Shutdown costs. "Draining" the pipeline.
At the start and end, some resources are unused.

## Slide 24: Pipelines Are Limited By Slowest Stage
What if Dry only took 20 mins, instead of 30?
Bora finishes Dry at 2:20.
But Andrew finishes Fold at 2:30. Bora still has to wait.
Pipeline rate is limited by the slowest pipeline stage.
 | 1:00 | 1:30 | 2:00 | 2:30 | 3:00 | 3:30 | 4:00
Andrew | Wash | Dry | Fold | Stash |  |  | 
Bora |  | Wash | Dry | Fold | Stash |  | 
Caroline |  |  | Wash | Dry | Fold | Stash | 
Dan |  |  |  | Wash | Dry | Fold | Stash

## Slide 25: Pipelining Laundry: Observations
Latency (time it takes to finish a single task) is unchanged.
It still took 2 hours for each person to do laundry.
Throughput (number of jobs finished per hour) increased.
Sequential: 4 people took 8 hours = 0.5 people per hour.
Pipelined: 4 people took 3.5 hours = 1.14 people per hour.
Maximum throughput speedup = number of stages.
If 4 people were doing laundry at any given time, we'd have 4x speedup.
Limited by cost of filling and draining pipeline at the start and end.
Pipeline rate is limited by the slowest pipeline stage.
Must wait for the slowest stage to finish before moving on to the next stage.
Balancing the length of each pipeline stage is good for speedup.

## Slide 26: Pipelining RISC-V Instructions
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 27: Pipeline Timing Diagrams
Example: In the third time step, the add instruction is in the Execute (EX) stage of the pipeline.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
add s0 t0 t1 | IF | ID | EX | M | WB |  |  |  |  | 
sub t2 s0 t0 |  |  |  |  |  | IF | ID | EX | M | WB
Sequence of instructions.
Numbers represent time steps.

## Slide 28: Sequential Instructions
Sequential approach: One instruction finishes, then the next one starts.
How long to run 2 instructions? 10 time steps.
How long to run each instruction? 5 time steps.
Our clock period would need to be 5 time steps.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
add s0 t0 t1 | IF | ID | EX | M | WB |  |  |  |  | 
sub t2 s0 t0 |  |  |  |  |  | IF | ID | EX | M | WB

## Slide 29: Pipelined Instructions
Pipelined approach: Multiple instructions in the circuit at the same time.
How long to run 2 instructions? 6 time steps.
How long to run each instruction? 5 time steps. (Same as before!)
Our clock period is now 1 time step!
 | 1 | 2 | 3 | 4 | 5 | 6
add s0 t0 t1 | IF | ID | EX | M | WB | 
sub t2 s0 t0 |  | IF | ID | EX | M | WB

## Slide 30: Pipelined Instructions
At any given moment in time, multiple instructions are in the circuit.
Different instructions are using different resources at the same time.
Example: At time step 3, the add instruction is using the Execute (EX) stage, while the sub instruction is using the Decode (ID) stage.
 | 1 | 2 | 3 | 4 | 5 | 6
add s0 t0 t1 | IF | ID | EX | M | WB | 
sub t2 s0 t0 |  | IF | ID | EX | M | WB

## Slide 31: Pipelined Instructions
Over time, each instruction passes through all 5 pipeline stages.
1 stage per clock cycle.
Note: The pipelined CPU uses one clock for all stages.
Clock cycle time is limited by the slowest stage (just like in the analogy).
 | 1 | 2 | 3 | 4 | 5 | 6
add s0 t0 t1 | IF | ID | EX | M | WB | 
sub t2 s0 t0 |  | IF | ID | EX | M | WB

## Slide 32: Pipelined Datapath
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 33: Pipelined Datapath
Recall: We split the datapath into 5 stages.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
inst[11:7]
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst[31:0]
PC
2
0
1
0
1
1
0
0
1
IMEM
PC
inst
ALU
PC+4
Instruction Fetch (IF)
Instruction Decode (ID)
Execute (EX)
Memory (M)
Write Back (WB)

## Slide 34: Pipelined Datapath
Add registers between each stage to "hold" a signal until the next clock cycle.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
inst[11:7]
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst[31:0]
PC
2
0
1
0
1
1
0
0
1
IMEM
PC
inst
ALU
PC+4
inst
PC+4
PC+4
RegReadData1
RegReadData2
inst
RegReadData2
ALU Out
PC+4
Reg Write Data
PC
PC

## Slide 35: Pipelined Datapath
Optimization: Recalculate PC+4 from PC in Memory stage to avoid storing/sending both PC and PC+4 down the pipeline.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst[31:0]
PC
2
0
1
0
1
1
0
0
1
IMEM
PC
ALU
PC
PC
RegReadData1
RegReadData2
inst
RegReadData2
ALU Out
Reg Write Data
+4
PC
inst[11:7]
inst
inst

## Slide 36: Pipelined Datapath
Send instructions down the pipeline so control logic operates correctly in each stage.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst (ID)
PC
2
0
1
0
1
1
0
0
1
IMEM
PC
ALU
PC
PC
RegReadData1
RegReadData2
inst
RegReadData2
ALU Out
Reg Write Data
+4
PC
inst[11:7]
inst
inst
inst (EX)
inst
inst (M)
inst
inst (WB)

## Slide 37: Pipelined Datapath
Change RegWriteIndex to use the rd field from the WB stage instruction, not the ID stage instruction.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst (ID)
PC
2
0
1
0
1
1
0
0
1
IMEM
PC
ALU
PC
PC
RegReadData1
RegReadData2
inst
RegReadData2
ALU Out
Reg Write Data
+4
PC
inst (EX)
inst
inst (M)
inst
inst (WB)
inst
inst
inst[11:7]

## Slide 38: Pipelining Control Logic
Approach #1: One control logic subcircuit per stage.
Store and send the instruction through the pipeline stages.
Calculate relevant signals in each stage.
Seen on the previous slides.
Approach #2: One control logic subcircuit.
Calculate all the control logic signals in the decode (ID) stage.
Send the control logic signals through the pipeline stages.

## Slide 39: Structural Hazards
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 40: Structural Hazards
Problem: Two or more instructions in the pipeline both need to access a single physical resource. In other words, a physical resource is needed in multiple stages.
Analogy example: What if the "Fold" and "Stash" tasks both needed the table?
Solution 1: Instructions take turns to use the resource.
Takes additional cycles per instruction.
One instruction must stall (wait) while the other uses the resource.
Solution 2: Add more hardware to machine.
Structural hazards can always be solved by adding more hardware.
Solution 3: Design the instruction set architecture (ISA) to avoid structural hazards.
RISC-V is designed like this.
Example: RegFile hardware can read two values per cycle. No RISC-V instruction needs to read 3 or more registers at once.

## Slide 41: Structural Hazard Example: Regfile
What are the physical limits of the Regfile?
It can read from 2 registers in a single cycle.
It can write to 1 register in a single cycle.
We avoid structural hazards by having separate "ports."
2 independent read ports, and 1 independent write port.
Allows 3 simultaneous accesses per cycle.
Hypothetical structural hazards:
What if the Regfile only had 1 read port?
What if a RISC-V instruction needed to write to 2 registers?
Good design helped us avoid structural hazards!
RegFile
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
RegReadData2
RegWEn

## Slide 42: Structural Hazard Example: Memory Access
The datapath has two memory blocks:
IMEM: Instruction Memory.
DMEM: Data Memory.
But they're really the same memory.
In a pipelined datapath, IMEM and DMEM are used at the same time. This is a structural hazard!
Solution 1: IF stage stalls a cycle while MEM uses memory.
Solution 2: Use two separate memories.
Solution 3: Use caches to make IMEM and DMEM appear like separate memories.
  This is what RISC-V does.
  More on caches later!
IMEM
PC
inst
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress

## Slide 43: Data Hazards
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 44: Data Hazards
When does add write to register s0? t = 5.
When does sub read the value in s0? t = 3.
Is this a problem?
 | 1 | 2 | 3 | 4 | 5 | 6
add s0 t0 t1 | IF | ID | EX | M | WB | 
sub t2 s0 t0 |  | IF | ID | EX | M | WB
Reminder: Regfile lives in the ID stage, so that's why the read happens in the ID stage.

## Slide 45: Data Hazards
Problem: An instruction depends on the result from the previous instruction.
The previous instruction hasn't finished executing yet...
...so the current instruction doesn't know the result to use!
Example: When sub reads s0, add has not updated s0 yet.
 | 1 | 2 | 3 | 4 | 5 | 6
add s0 t0 t1 | IF | ID | EX | M | WB | 
sub t2 s0 t0 |  | IF | ID | EX | M | WB

## Slide 46: Data Hazard Example (1/2)
Does this code have a data hazard?
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
add t0 t1 t2 | IF | ID | EX | M | WB |  | 
or t3 t4 t5 |  | IF | ID | EX | M | WB | 
slt t6 t0 t3 |  |  | IF | ID | EX | M | WB

## Slide 47: Data Hazard Example (1/2)
To identify data hazards: Check if we write to a register and then read from it later.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
add t0 t1 t2 | IF | ID | EX | M | WB |  | 
or t3 t4 t5 |  | IF | ID | EX | M | WB | 
slt t6 t0 t3 |  |  | IF | ID | EX | M | WB

## Slide 48: Data Hazard Example (1/2)
To identify data hazards: Check if we write to a register and then read from it later.
add writes to t0 at t = 5.
slt reads from t0 at t = 4. This is too early to get the updated value!
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
add t0 t1 t2 | IF | ID | EX | M | WB |  | 
or t3 t4 t5 |  | IF | ID | EX | M | WB | 
slt t6 t0 t3 |  |  | IF | ID | EX | M | WB

## Slide 49: Data Hazard Example (2/2)
Does this code have a data hazard?
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add t0 t1 t2 | IF | ID | EX | M | WB |  |  |  | 
or t3 t4 t5 |  | IF | ID | EX | M | WB |  |  | 
slt t6 t2 t3 |  |  | IF | ID | EX | M | WB |  | 
lw t3 4(t0) |  |  |  | IF | ID | EX | M | WB | 
add t0 t1 t2 |  |  |  |  | IF | ID | EX | M | WB

## Slide 50: Data Hazard Example (2/2)
To identify data hazards: Check if we write to a register and then read from it later.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add t0 t1 t2 | IF | ID | EX | M | WB |  |  |  | 
or t3 t4 t5 |  | IF | ID | EX | M | WB |  |  | 
slt t6 t2 t3 |  |  | IF | ID | EX | M | WB |  | 
lw t3 4(t0) |  |  |  | IF | ID | EX | M | WB | 
add t0 t1 t2 |  |  |  |  | IF | ID | EX | M | WB

## Slide 51: Data Hazard Example (2/2)
To identify data hazards: Check if we write to a register and then read from it later.
add writes to t0 at t = 5.
lw reads from t0 at t = 5. Is that too early?
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add t0 t1 t2 | IF | ID | EX | M | WB |  |  |  | 
or t3 t4 t5 |  | IF | ID | EX | M | WB |  |  | 
slt t6 t2 t3 |  |  | IF | ID | EX | M | WB |  | 
lw t3 4(t0) |  |  |  | IF | ID | EX | M | WB | 
add t0 t1 t2 |  |  |  |  | IF | ID | EX | M | WB

## Slide 52: Data Hazard Example (2/2)
Some regfiles support writing a new value to a register, and then reading the new value, in the same cycle.
Not all regfiles support this. Check assumptions in any question.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add t0 t1 t2 | IF | ID | EX | M | WB |  |  |  | 
or t3 t4 t5 |  | IF | ID | EX | M | WB |  |  | 
slt t6 t2 t3 |  |  | IF | ID | EX | M | WB |  | 
lw t3 4(t0) |  |  |  | IF | ID | EX | M | WB | 
add t0 t1 t2 |  |  |  |  | IF | ID | EX | M | WB

## Slide 53: Fixing Data Hazards: Stalling
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 54: Fixing Data Hazards
Solution 1: Stalling.
Wait for the first instruction to write its result before the second instruction reads the value.
Solution 2: Forwarding.
Add hardware to directly send the result back to the earlier stage, before the result is even written.
Solution 3: Code Scheduling.
Rearrange instructions to avoid data hazards.

## Slide 55: Stalling
Without stalling, we have a data hazard:
add writes to t0 at t = 5.
slt reads from t0 at t = 4 (too early to get the updated value).
We need slt to wait 2 time steps before reading t0.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
add t0 t1 t2 | IF | ID | EX | M | WB |  | 
or t3 t4 t5 |  | IF | ID | EX | M | WB | 
slt t6 t0 t3 |  |  | IF | ID | EX | M | WB

## Slide 56: Stalling
Now, the read happens after the write. No more hazard!
add writes to t0 at t = 5.
slt reads from t0 at t = 6. The correct updated value is read!
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add t0 t1 t2 | IF | ID | EX | M | WB |  |  |  | 
nop |  | IF | ID | EX | M | WB |  |  | 
nop |  |  | IF | ID | EX | M | WB |  | 
or t3 t4 t5 |  |  |  | IF | ID | EX | M | WB | 
slt t6 t0 t3 |  |  |  |  | IF | ID | EX | M | WB

## Slide 57: Stalling
To stall, we add no-ops into the code to delay an instruction.
Recall: A no-op is an instruction that does nothing.
  Example: addi x0 x0 0.
  nop is a pseudo-instruction you can type in RISC-V.
Compiler can insert no-ops to avoid data hazards.
  Requires the compiler to know about the pipeline structure.
Stalls reduce performance, but they're required to get correct results!

## Slide 58: Fixing Data Hazards: Forwarding
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 59: Forwarding Example (1/2)
Problem: add writes t0 at t = 5, which is too late.
Idea: When do we first learn the result of the add computation?
 | 1 | 2 | 3 | 4 | 5 | 6
add t0 t1 t2 | IF | ID | EX | M | WB | 
slt t6 t0 t3 |  | IF | ID | EX | M | WB

## Slide 60: Forwarding Example (1/2)
Problem: add writes t0 at t = 5, which is too late.
Idea: When do we first learn the result of the add computation?
At t = 3, we already know the value that will be written to t0.
We can add hardware to forward this value so that slt can use it directly.
 | 1 | 2 | 3 | 4 | 5 | 6
add t0 t1 t2 | IF | ID | EX | M | WB | 
slt t6 t0 t3 |  | IF | ID | EX | M | WB

## Slide 61: Forwarding
Idea: Use the result as soon as it's computed.
Read the value directly from a wire in the datapath.
Don't wait for the result to be written to a register (and then read back).
Forwarding requires extra connections in the datapath.
We need extra wires to forward values to earlier stages.
We need extra logic to check if forwarding is needed.
  Where is the current instruction writing to? (i.e. what is rd?)
  Where is the next instruction reading from? (i.e. what is rs1/rs2?)
  If they're the same register*, we need to forward.
*Be careful to ignore writes to x0. If the current instruction is writing to x0, there's no data hazard, because writes to x0 do nothing.

## Slide 62: Adding Forwarding to Datapath (1/2)
This wire forwards the ALU result, so the next instruction can use result as ALU input.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst (ID)
PC
2
0
1
0
1
0
1
IMEM
PC
ALU
PC
PC
RegReadData1
RegReadData2
inst
RegReadData2
ALU Out
Reg Write Data
+4
PC
inst (EX)
inst
inst (M)
inst
inst (WB)
inst
inst
inst[11:7]

## Slide 63: Forwarding Example (2/2)
Problem: lw writes to s2 at t = 5, which is too late.
Idea: When do we first learn the result of the load?
 | 1 | 2 | 3 | 4 | 5 | 6
lw s2 20(s1) | IF | ID | EX | M | WB | 
add s4 s2 s5 |  | IF | ID | EX | M | WB

## Slide 64: Forwarding Example (2/2)
Problem: lw writes to s2 at t = 5, which is too late.
Idea: When do we first learn the result of the load?
The value from memory shows up at t = 4.
That's too late to send the value into the ALU!
We have to stall for one cycle.
 | 1 | 2 | 3 | 4 | 5 | 6
lw s2 20(s1) | IF | ID | EX | M | WB | 
add s4 s2 s5 |  | IF | ID | EX | M | WB

## Slide 65: Forwarding Example (2/2)
Problem: lw writes to s2 at t = 5, which is too late.
Idea: When do we first learn the result of the load?
The value from memory shows up at t = 4.
That's too late to send the value into the ALU!
We have to stall for one cycle.
Now, we can add hardware to forward the value so add can use it directly.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
lw s2 20(s1) | IF | ID | EX | M | WB |  | 
nop |  | IF | ID | EX | M | WB | 
add s4 s2 s5 |  |  | IF | ID | EX | M | WB

## Slide 66: Adding Forwarding to Datapath (2/2)
This wire forwards the value read from memory, so the next instruction can use the value as ALU input.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst (ID)
PC
2
0
1
0
1
0
1
IMEM
PC
ALU
PC
PC
RegReadData1
RegReadData2
inst
RegReadData2
ALU Out
Reg Write Data
+4
PC
inst (EX)
inst
inst (M)
inst
inst (WB)
inst
inst
inst[11:7]

## Slide 67: Adding Forwarding Control Logic to Datapath
We need extra control logic to check whether we need to apply forwarding.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst (ID)
PC
2
0
1
0
1
0
1
IMEM
PC
ALU
PC
PC
RegReadData1
RegReadData2
inst
RegReadData2
ALU Out
Reg Write Data
+4
PC
inst (EX)
inst
inst (M)
inst
inst (WB)
inst
inst
inst[11:7]
inst (ID)

## Slide 68: Fixing Data Hazards: Code Scheduling
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 69: Code Scheduling
Stalling inserts no-ops, which causes performance loss.
Idea: The compiler could use that no-op slot to execute an unrelated instruction.
In other words, we reorder code to avoid data hazards.
Requires the compiler to know about the pipeline structure.

## Slide 70: Code Scheduling Example
Consider this C code:
Load A[0] | lw t0 0(a0)
Load A[1] | lw t1 4(a0)
A[0]+A[1] | add t3 t0 t1
Store A[3] | sw t3 12(a0)
Load A[2] | lw t2 8(a0)
A[0]+A[2] | add t4 t0 t2
Store A[4] | sw t4 16(a0)
Load A[0] | lw t0 0(a0)
Load A[1] | lw t1 4(a0)
Load A[2] | lw t2 8(a0)
A[0]+A[1] | add t3 t0 t1
Store A[3] | sw t3 12(a0)
A[0]+A[2] | add t4 t0 t2
Store A[4] | sw t4 16(a0)
A[3] = A[0] + A[1]; A[4] = A[0] + A[2];
Original instruction order: 2 data hazards.
After reordering the "Load A[2]" instruction: 0 data hazards.

## Slide 71: Control Hazards
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 72: Control Hazards
If the branch is taken (t0 == t1), when do we figure out where to branch to?
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
beq t0 t1 Label | IF | ID | EX | M | WB |  |  |  | 
sub t2 s0 t0 |  | IF | ID | EX | M | WB |  |  | 
add t6 s0 t3 |  |  | IF | ID | EX | M | WB |  | 
xor t5 t1 s0 |  |  |  | IF | ID | EX | M | WB | 
sw s0 8(t3) |  |  |  |  | IF | ID | EX | M | WB

## Slide 73: Control Hazards
Recall: The EX stage is where we compute where to branch to.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst (ID)
PC
2
0
1
0
1
1
0
0
1
IMEM
PC
ALU
PC
PC
RegReadData1
RegReadData2
inst
RegReadData2
ALU Out
Reg Write Data
+4
PC
inst (EX)
inst
inst (M)
inst
inst (WB)
inst
inst
inst[11:7]

## Slide 74: Control Hazards
If the branch is taken (t0 == t1), when do we figure out where to branch to?
At t = 3, the branch instruction runs the EX stage, which tells us where to go.
But at t = 3, two more unwanted instructions have entered the pipeline!
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
beq t0 t1 Label | IF | ID | EX | M | WB |  |  |  | 
sub t2 s0 t0 |  | IF | ID | EX | M | WB |  |  | 
add t6 s0 t3 |  |  | IF | ID | EX | M | WB |  | 
xor t5 t1 s0 |  |  |  | IF | ID | EX | M | WB | 
sw s0 8(t3) |  |  |  |  | IF | ID | EX | M | WB

## Slide 75: Control Hazards
If the branch is taken, we're going somewhere else.
We do not want to execute sub and add.
We need to convert the next two instructions after the branch to no-ops.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
beq t0 t1 Label | IF | ID | EX | M | WB |  |  |  | 
sub t2 s0 t0 |  | IF | ID | EX | M | WB |  |  | 
add t6 s0 t3 |  |  | IF | ID | EX | M | WB |  | 
xor t5 t1 s0 |  |  |  | IF | ID | EX | M | WB | 
sw s0 8(t3) |  |  |  |  | IF | ID | EX | M | WB

## Slide 76: Control Hazards
If a branch is not taken:
The instructions fetched after the branch are correct.
There's no control hazard.
If the branch is taken, or if there's a jump:
The next two instructions in the pipeline are incorrect.
There's a control hazard!
To fix, we need to convert the incorrect instructions in the pipeline to no-ops.
This fix is called flushing the pipeline.

## Slide 77: Branch Prediction
Problem: Every time we take a branch or jump, we lose 3 cycles to no-ops.
Solution: Branch prediction.
Try and guess whether the branch will be taken.
Only flush the pipeline if we guess wrong.
Branch prediction improves performance on average, but there's still a penalty for wrong guesses.
What does our datapath do?
Naive prediction: Our datapath always guesses "not taken" and fetches the next instructions.

## Slide 78: Pipelined Datapath
Note: We lose 3 cycles on a branch/jump, because updated PC is written back in MEM stage. While this happens, 3 instructions are in pipeline and need to be flushed.
Branch Comp
Imm Gen
RegFile
+4
BSel
RegWriteData
RegWriteIndex
RegReadIndex1
RegReadIndex2
RegReadData1
ALU
PC+4
Mem
RegReadData2
inst[24:20]
inst[19:15]
ALU
A
B
ASel
BrEq
BrLT
BrUn
DMEM
MemWEn
MemReadData
MemWriteData
MemAddress
ALUSel
ImmSel
RegWEn
MemRW
WBSel
RegWEn
PC+4
ALU
PCSel
inst (ID)
PC
2
0
1
0
1
1
0
0
1
IMEM
PC
ALU
PC
PC
RegReadData1
RegReadData2
inst
RegReadData2
ALU Out
Reg Write Data
+4
PC
inst (EX)
inst
inst (M)
inst
inst (WB)
inst
inst
inst[11:7]

## Slide 79: Superscalar Processors
Measuring Performance
Pipelining
Analogy: Laundry
Pipelining RISC-V Instructions
Pipelined Datapath
Hazards
Structural Hazards
Data Hazards
Fixing Data Hazards: Stalling
Fixing Data Hazards: Forwarding
Fixing Data Hazards: Scheduling
Control Hazards
Superscalar Processors
Lectures 21–22, CS 61C, Fall 2024

## Slide 80: Pipelining and ISA Design
The RISC-V ISA is designed for pipelining.
All instructions are 32 bits wide.
  Easy to fetch in one clock cycle, and decode in one clock cycle.
  Contrast with CISC (R = Reduced, C = Complex) ISAs like x86: Instructions can be 1–15 bytes wide!
There's a small set of standard instruction formats.
  Can decode instruction and read from registers in one stage.
Load/store addressing is conceptually simple.
  In Stage 3 (EX), use the ALU to compute the address.
  In Stage 4 (MEM), access memory.
Memory operands are all aligned.
  Memory access only takes one cycle.
The 5-stage pipeline is commonplace in many devices: Cars, appliances, etc.

## Slide 81: Further Increasing Processor Performance?
1. Increase clock rate.
Limited by technology and power dissipation.
2. Increase pipeline depth.
"Overlap" instruction execution through deeper pipeline, e.g. 10 or 15 stages.
Less work per stage means shorter clock cycles and lower power.
But more potential for all 3 types of hazards!
More hazards means more stalling. Cycles per instruction > 1.
3. Design a superscalar processor.
Desktops, laptops, cell phones, etc. often have a few of these, combined with simpler 5-stage pipeline processors.

## Slide 82: Superscalar Processors
Multiple-issue: Start multiple instructions per clock cycle.
Multiple execution units execute instructions in parallel.
Each execution has its own pipeline.
CPI < 1: Multiple instructions completed per clock cycle.
Dynamic "out-of-order" execution:
Reorder instructions dynamically in hardware to reduce impact of hazards.
Take CS 152 to learn more!

## Slide 83: Computing Cycles Per Instruction (CPI)
How do we measure CPI?
In practice, we measure CPI on various benchmarks.
There are benchmark programs from a variety of application domains: Data compression, code compilation, video decoding, network simulation, etc.
Time | = | Instructions | Cycles | Time
Program |  | Program | Instruction | Cycle
Recall the "Iron Law" of processor performance:
Can measure.
Can count.
1/clock rate.
Cycles | = | Time | ÷ | Instructions | × | Time
Instruction |  | Program |  | Program |  | Cycle
Rearrange terms to solve for CPI:

## Slide 84: ARM A53 Benchmark
ARM Cortex-A53 Core: 2 GHz, dual-issue processor:
4 BIPS (billion instructions per second).
Peak CPI = 0.5.
However, instruction/pipeline dependencies reduce performance.
If CPI < 1, we can also measure in terms of IPC (Instructions Per Cycle).
More about parallelism and performance later in CS 61C!